## Slide 1: Risk and Resilience, Clinical presentation, and Biomarker Profiles of Chronic Traumatic Encephalopathy and Related Dementias: The DIAGNOSE CTE Research Project II (DxCTE-II)
Biospecimen collection & processing

## Slide 2: Overview
  Specimen uniformity and quality
  Site Equipment
  Procedures
    Kit Contents and Ordering
    Sample Labelling
    Sample Collection and Processing
    Shipping Samples
    Non-Conformance
  Contact Information

## Slide 3: Specimen Uniformity and Quality
General reminders

## Slide 4: Specimen Standardization and Quality
Most biomarkers are sensitive to time and temperature
  Standardization of processing across sites is key
  Specimens must be processed within 2 hours of collection
  Reference the BioSEND Biomarker Specimen Collection, Processing, and Shipment Manual as needed
  Do not replace or supplement any kit components without first receiving approval from BioSEND/NINDS
  Questions? Email biosend@iu.edu

## Slide 5: Site Consumables and Equipment
Gloves
Alcohol wipes
Butterfly needles
Tourniquet
Gauze pads
Bandages
Microcentrifuge tube rack
Sharps bin and lid
Crushed ice
Pipettes and pipette tips
Centrifuge capable of maintaining 4°C
-80°C Freezer
Dry ice
Sites will need to supply the following items:

## Slide 6: Procedures
Maintaining specimen uniformity and quality

## Slide 7: Biospecimen Collection Protocol
Collection Tube | Drawn At | Specimen Type | Aliquot Volume | Total Number of Aliquots | Cryovial Cap Color | Shipping Temperature
4 EDTA (plastic) Blood Collection Tubes, 10ml | BL | Plasma | 1.5ml | 12 | Purple | Frozen
 | BL | Buffy Coat | ~750ul | 4 | Clear | Frozen

## Slide 8: Kit Contents and Ordering
All sites will be sent a Supplemental Kit with their first kit shipment
    Contains extra blood collection tubes and processing supplies
    May be used to replace items in study visit kits
Study Visit Kits should be ordered as soon as visits are planned
    Contains collection, processing, and shipping supplies specific to each visit
    Includes barcoded labels
    The supplies/labels in each study visit kit are intended for that visit only

## Slide 9: Kit Contents and Ordering – REDCap Survey
  https://redcap.link/dxcteIIkits
  Order kits online through the Kit Request Module for:
  Blood kits
  Shipping kits
  Extra Supplies
  Please provide as much notice as possible when ordering kits and/or supplies.

## Slide 10: Kit Contents and Ordering: Confirm Site Info
DxCTE-II Kit Request Module
Select your site from the drop-down list
Verify contact information and update if needed

## Slide 11: Kit Contents and Ordering: Kit Types
DxCTE-II Kit Request Module
Kits are not specific to a subject or time point. After collection, sites will indicate the subject and time point to which BioSEND should link the samples.
Standard collection kit for plasma and buffy coat contains supplies for one subject-visit.
Shipping Kits are ordered independently of Blood Kits
A single Shipping Kit may be used to send samples for 1-2 cryoboxes

## Slide 12: Kit Contents and Ordering: Kit Breakdown
DxCTE-II Kit Request Module
Kit contents of selected kit will appear at the bottom of the page

## Slide 13: Kit Contents and Ordering: Kits
  Blood Kit (frozen):
  Shipping Kit:

## Slide 14: Kit and Supply Ordering
Click “Submit” to send order to BioSEND; staff will confirm receipt of your order
Please allow two week turn-around time for kit shipments
If urgent request needed, please note date needed by in comments and email BioSEND. We cannot guarantee urgent orders, but we will do our best to accommodate.
BioSEND will send confirmation of shipment and tracking number when supplies ship

## Slide 15: Sample Labelling: Example Labels
  Labels are provided by Indiana University
  Please check that all samples are properly labelled to ensure correct identification by IU
  If do not have enough labels to complete a visit, please contact IU immediately
  Labelling the tubes during processing prevents sample mix-ups
Notes: It can be difficult to stick the label on a cold or wet tube.

## Slide 16: Sample Labelling: Label Placement
Please...
Label all collection and aliquot tubes before cooling, collecting, processing, or freezing samples
Label only 1 subject’s tubes at a time to avoid mix-ups
Wrap the label around the tube horizontally - label position is important for all tube types
Make sure the label is completely adhered by rolling between your fingers
0001234567
BioSEND
987654
PLASMA
0001234567
BioSEND
987654
PLASMA
YES
NO

## Slide 17: Collection Volumes
Total blood volumes
Sample Type | Amount
Whole Blood for Plasma and Buffy Coat | 40 ml

## Slide 18: Sample Collection and Processing
Supplies provided for the collection of plasma and buffy coat
K2 EDTA tube
4 x 10ml EDTA (plastic) collection tubes
12 x 2ml Cryovials (purple-capped) for plasma aliquots
4 x 2ml Cryovials (clear-capped) for buffy coat aliquots
K2 EDTA tube
K2 EDTA tube
K2 EDTA tube

## Slide 19: Sample Collection and Processing: Plasma & Buffy Coat
*We recognize that the processing timeline provided in this SOP may not be possible for all visits, and sample centrifugation may begin later than recommended. As long as the samples are processed and frozen within 2 hours, it is not considered a protocol deviation.
Step One
Step Two
Step Four
Step Five
Collect blood in EDTA tubes; allow blood to flow for 10 seconds and ensuring blood flow has stopped
Immediately after blood draw, GENTLY invert tubes 8-10 times to mix
Store tubes at room temperature
Label 4 collection tubes with preprinted “COLLECT WBLD EDTA10” labels prior to blood draw
Within 30 minutes of blood draw, centrifuge sample at 1500 x g at 4˚C for 15 minutes.
Plasma
Step Six
Using a clean transfer pipet, aliquot 1.5 ml plasma into each purple-capped cryotube.
Plasma
Label 12 purple-capped cryotubes with “ALIQUOT PLASMA EDTA10” labels and 4 clear capped crytotubes with “ALIQUOT BUFFY EDTA10” labels.
Pre-chill cryotubes on wet ice for at least 5 minutes
Step Three
Step Seven
Using a clean transfer pipet, collect the buffy coat – should appear pink or red due to residual plasma and red blood cells
Transfer the buffy coat from each EDTA tube into a clear-capped cryotube
Store plasma & buffy coat at -80 until shipment
K2 EDTA tube
K2 EDTA tube
Buffy
coat

## Slide 20: Sample Collection and Processing: Aliquots
Filling biomarker plasma aliquots:
Fill as many cryovials as possible to 1.5 ml (plasma)
Over-filled vials may burst in freezer!
Ship ALL material to IU, even if final vial is less than standard volume
YES
NO

## Slide 21: Sample Collection and Processing: Timeline
Timeline for blood processing
Blood Collection
15-30 Minutes
Invert all tubes 8x to mix
Centrifuge EDTA tubes
Aliquot plasma
90-120 Minutes
Freeze plasma, and buffy coat aliquots
Aliquot buffy coats

## Slide 22: Sample Collection and Processing: Issue #1
  Troubleshooting Blood Collection
  Issue #1: Tube with little/no vacuum
  Always check expiration date on the tube before beginning blood draw and discard expired tubes
  Store tubes at “room temperature” – extreme temperature can affect vacuum
  Keep extra vacutainer tubes from supplemental kit nearby during blood draw to replace “bad” tubes
  If this is a frequent occurrence, report tube type and lot number to IU.

## Slide 23: Sample Collection and Processing: Issue #2
  Troubleshooting Blood Collection
  Issue #2: Hemolyzed plasma caused by incorrect collection
For more information, visit: http://www.bd.com/vacutainer/pdfs/techtalk/TechTalk_Jan2004_VS7167.pdf
Notes: Don’t move needle around in the vein

## Slide 24: Sample Collection and Processing: Issue #2 continued
  Troubleshooting Blood Collection
  Issue #2: Hemolyzed plasma caused by incorrect processing
For more information, visit: http://www.bd.com/vacutainer/pdfs/techtalk/TechTalk_Jan2004_VS7167.pdf
Notes: Let the serum clot!

## Slide 25: Sample Collection and Processing Form
Specimen Collection and Processing Form
Direct Link for Duke:
https://redcap.link/DXCTEIISampleForm
First page captures basic subject and visit information

## Slide 26: Sample Collection and Processing Form
Second page captures processing information

## Slide 27: Sample Collection and Processing Form
PDF form of responses will be emailed to you. Print a copy of the Frozen Shipping Manifest and include with shipment.

## Slide 28: Sample Collection and Processing Form
  Submission of the Shipping Manifest portion of the form serves as shipment notification to BioSEND
  Must be completed prior to shipment
  If samples are shipped and not received, BioSEND will follow-up with courier. It is recommended that sites also track shipment to ensure safe delivery

## Slide 29: Shipping Samples
Packing and Shipping Frozen Samples
  UPS Dry Ice label should not be covered with other stickers and must be completed, or UPS will reject/return your package!

## Slide 30: Shipping Frozen Samples: Tips
  Packing and Shipping Frozen Samples
  All DxCTE-II samples ship frozen
  Ship frozen samples on dry ice
  Frozen samples should be shipped only Monday through Wednesday
  Always fill carton to top with dry ice
  Do not pack shipment until the day of pickup
Notes: Cap at Wednesday because of concerns about delay – additional instructions around holidays
Make sure to put the weight on the blue dry ice label and don’t cover it with anything

## Slide 31: Shipping Samples: Frozen
Do not ship more than 2 biohazard bags in a single shipper (equivalent to two subject-visits).
  Allows room for dry ice to keep samples frozen in transit
  Minimizes loss in the rare but unfortunate event of courier issues

## Slide 32: Shipping Samples – UPS: https://kits.iu.edu/UPS
Search for address
Enter weight
Click “Ship”
Choose Study
Schedule Pickup

## Slide 33: Shipping Samples via UPS
IU UPS ShipExec Shipping Portal
Print out UPS air waybill
Ensure all elements (barcode, return address, etc.) printed clearly
Fold and insert UPS air waybill into clear plastic sleeve on package

## Slide 34: Shipping Samples: Closures
Please also consider weather when shipping. UPS will post service updates on their webpage. Reach out to BioSEND if you an unsure if it is safe to ship.
Date | Holiday
January 1 | New Year's Day
3rd Monday in January | Martin Luther King, Jr Day
4th Monday in May | Memorial Day
June 19 | Juneteenth (observed)
July 4 | Independence Day (observed)
1st Monday in September | Labor Day
4th Thursday in November | Thanksgiving
4th Friday in November | Friday after Thanksgiving
December 25 | Christmas
Notes: Note that we are closed to shipments on these days and also will not be able for questions/supply requests. We have extended closures at the end of the year to help keep our samples out of the fray of courier overload around the holidays. We close for shipments the week of Thanksgiving and the last two weeks of the year through the first business day of the New Year. We will add your email to our contact list that we use to send reminders about these extended closures. If you’re ever unsure about whether or not it’s okay to ship, you can reach out to us and we can make that call for you.

## Slide 35: Non-Conformance
  Non-conformance to standard procedures may reduce the utility of the biospecimens:
  Not processing plasma within 2 hours of collection allows for breakdown of certain proteins and small molecules
  Over/under centrifuging changes plasma composition

## Slide 36: Non-Conformance Reporting con’t
  Most common non-conformance issues:
  Shipment notification not sent
  Samples shipped for weekend/holiday delivery
  Sample form incomplete/inaccurate
  Low volume
  Unlabeled or mislabeled tube(s)
  Sample hemolysis

## Slide 37: Non-Conformance and Inventory Reporting
  Most common non-conformance issues:
  BioSEND will notify sites directly of any issues upon receipt
  BioSEND will email sites a monthly inventory report of all samples received from that site to date
  If you are experiencing issues, please reach out to us for help! It is much easier to prevent an issue before sample collection & shipment than trying to fix it after the fact

## Slide 38: BioSEND.org
On the website, you can:
Access your study’s kit request module and sample submission form
Download the most recent version of the Manual of Procedures
View a recording of this training
Find information about holiday closures
Access shipping resources

## Slide 39: Contacts
  Indiana University
  General Questions/Shipment Notifications:
  biosend@iu.edu
  317-278-6158
Request kits:
https://redcap.link/dxcteIIkits